McGill University

Department of Electrical and Computer  Engineering

Course: ECSE 323  -Digital Systems Design				Fall 2008

ASSIGNMENT #1

(with solutions)

# TOPIC:  BOOLEAN LOGIC THEORY

1.-      Prove the validity of the following identity

((C + ABD +(BD +(AB)(C + AB +BD) = B(A + C)((A +(C) + D(B +C)

State the axioms and theorems of Boolean algebra you used in the process.

Hint: Use distributive, complementation, absorption, null element, commutative, simplification.

___________________________________________________________________________

ANSWER

((C + ABD +(BD +(AB)(C + AB +BD) = B(A + C)((A + C) + D(B +C)

L.H.S.  =  C(C + A B(C + B(C D + ABCD +ABD + ABD +(BCD

+ A B(B D + B(B D + (A B C + A(A B +(A B B D                 (Distributive)

=  0 + A B(C + B(C D + A B D (C + 1) + A B D +(B C D

+ 0 + 0 +(A B C + 0 +(A B D                                            (Complement +

Distributive +

Absorption)

=  A B(C + B(C D + A B D +(B C D +(A B C +(A B D      Null element

=  A B(C + B(C D + BD(A +(A) +(B C D +(A B C          (Distributive +

Complement +

Commutative)

= A B(C + BD((C + 1) +(B C D +(A B C     (Distributive + Absorption)

= A B(C + (B +(B C)D +(A B C                    (Distributive)

=  A B(C + (B + C)D +(A B C                        (Simplify)

= A B(C + (A B  C + D(B + C)

= B(A + C)((A +(C) + D(B + C)      =   R.H.S.

__________________________________________________________________________

2.-     a)  Given the following function  F  by its truth table, produce the truth table of  FD , where  FD is the dual of  F .

| A B C | F |
| --- | --- |
| 0 0 0 | 0 |
| 0 0 1 | 1 |
| 0 1 0 | 0 |
| 0 1 1 | 1 |
| 1 0 0 | 1 |
| 1 0 1 | 0 |
| 1 1 0 | 0 |
| 1 1 1 | 1 |

b)  Using K-maps, show that the complement of the dual of the function  F  in part a) is identical to the dual of its complement.

__________________________________________________________________________

ANSWER

a)

According to the definition of duality, we change ALL 0’s  into  1’s and  ALL 1’s into 0’s

| A B C | FD |
| --- | --- |
| 1 1 1 | 1 |
| 1 1 0 | 0 |
| 1 0 1 | 1 |
| 1 0 0 | 0 |
| 0 1 1 | 0 |
| 0 1 0 | 1 |
| 0 0 1 | 1 |
| 0 0 0 | 0 |
| A B C | F |
| 0 0 0 | 0 |
| 0 0 1 | 1 |
| 0 1 0 | 0 |
| 0 1 1 | 1 |
| 1 0 0 | 1 |
| 1 0 1 | 0 |
| 1 1 0 | 0 |
| 1 1 1 | 1 |

b)

| AB C | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 0 | 0 | 1 | 0 | 0 |
| 1 | 1 | 0 | 1 | 1 |
| AB C | 00 | 01 | 11 | 10 |
| 0 | 1 | 0 | 1 | 1 |
| 1 | 0 | 1 | 0 | 0 |

FD                                                                                               ____

(FD)

| AB C | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 0 | 1 | 1 | 1 | 0 |
| 1 | 0 | 0 | 0 | 1 |
| AB C | 00 | 01 | 11 | 10 |
| 0 | 1 | 0 | 1 | 1 |
| 1 | 0 | 1 | 0 | 0 |

(F  = (A(C + B(C + A(B C                                     ((F )D = ((A +(C)(B +(C)(A +(B + C)

____					           = (A B C +(C A +(C B

Therefore,   (FD) = ((F )D .

3.-  Consider the following function,  F,  of four variables

F(A,B,C,D) = (m(4,5,7,12,14,15) +  (d(3,8,10)

where (d represent the don’t care values of the function  f.

a)  Give the minimal sum-of-products form of  f.

b) Give the minimal product-of-sums form of  f.

________________________________________________________________________

ANSWER

a)                                                                   b)

| AB CD | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 0 | 1 | 1 | X |
| 01 | 0 | 1 | 0 | 0 |
| 11 | X | 1 | 1 | 0 |
| 10 | 0 | 0 | 1 | X |
| AB CD | 00 | 01 | 11 | 10 |
| 00 | 0 | 1 | 1 | X |
| 01 | 0 | 1 | 0 | 0 |
| 11 | X | 1 | 1 | 0 |
| 10 | 0 | 0 | 1 | X |

Minimal sum-of-products                              Minimal product-of-sums

F = A(D  + B C D +(A  B(C                     F = B ((A + C +(D )( A +(C + D )

________________________________________________________________4.-          Consider the following Boolean function

F (A,B,C,D) = ∑m(1,4,6,7,8,9,10,11,15).

a) 	List all the prime implicants of  F  by following the Quine-McCluskey

method.

b)       Give all minimal two-level sum-of-products expressions of  F  by showing the                                                 covering table and by using the Petrick function.

c)	Minimize the function using a k-map and verify that you obtain the same answer as in part b).

___________________________________________________________________________

ANSWER

a)

First reduction

| ID | ABCD |
| --- | --- |
| 1 ( | 0 0 0 1 |
| 4 ( | 0 1 0 0 |
| 8 ( | 1 0 0 0 |
| 6 ( | 0 1 0 1 |
| 9 ( | 1 0 0 1 |
| 10 ( | 1 0 1 0 |
| 7 ( | 0 1 1 1 |
| 11 ( | 1 0 1 1 |
| 15 ( | 1 1 1 1 |
| Group | ABCD |
| (1,4) | - 0 0 1 |
| (4,6) | 0 1 - 0 |
| (6,7) | 0 1 1 - |
| (7,15) | - 1 1 1 |
| (11,15) | 1 - 1 1 |
| (8,9) ( | 1 0 0 - |
| (10,11) ( | 1 0 1 - |
| Group | ABCD |
| (8,9,10,11) | 1 0 - - |

Second and final reduction

List of prime implicants

| ABCD | Group | Terms |
| --- | --- | --- |
| - 0 0 1 | (1,4) | (B(C D |
| 0 1 - 0 | (4,6) | (A B(D |
| 0 1 1 - | (6,7) | (A B C |
| - 1 1 1 | (7,15) | B C D |
| 1 - 1 1 | (11,15) | A C D |
| 1 0 - - | (8,9,10,11) | A(B |

Covering table

Minterms

| ABCD | Group | 1 4 6 7 8 9 10 11 15 |
| --- | --- | --- |
| - 0 0 1 | (1,4) P1 | X X |
| 0 1 - 0 | (4,6) P2 | X X |
| 0 1 1 - | (6,7) P3 | X X |
| - 1 1 1 | (7,15) P4 | X X |
| 1 - 1 1 | (11,15) P5 | X X |
| 1 0 - - | (8,9,10,11) P6 | X X X X |

Essential prime implicants:  (B (C D,  (A  B C, A(B

Petrick Function

P = P1 P2 (P2 + P3)(P3 + P4)P6(P1 + P6)P6(P5 + P6)(P4 + P5)

= P1 P2 P6 (P2P4 + P3)(P1P5 + P6)(P3P5 + P4)

= P1P2P6(P2P4P1P5 + P2P4P6 + P3P1P5 + P3P6)(P3P5 + P4)

= P1P2P6(P1P2P3P4P5 + P2P3P4P5P6 + P1P3P5 + P3P5P6  + P1P2P4P5 + P2P4P6 + P1P3P4P5 + P3P4P6)

=  P1P2P6P4 + P1P2P3P5P6 + ….

Fmin = P1 + P2 + P6 + P4  = (B(C D + (A B(D + A(B + B C D.

c)

| AB CD | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 0 | 1 | 0 | 1 |
| 01 | 1 | 0 | 0 | 1 |
| 11 | 0 | 1 | 1 | 1 |
| 10 | 0 | 1 | 0 | 1 |

Fmin = (B(C D + (A B(D + B C D + A(B

which is the same as the one obtained in  part b).

__________________________________________________________________________

5.-   When a function, T, is expanded about one of its variables, say  X , the resulting expression can be written in the form  T = X R1 +(X  R2 , where R1 and R2 are called residue functions of  T and are independent of  the variable  X.

a)  What is the condition that the residue functions must satisfy for  T  to be independent of  X  but dependent of  (X ?

b) What is the condition that the residue functions must satisfy for  T  to be independent of (X  but dependent of  X ?

c) What is the condition that the residue functions must satisfy for  T  to be independent of  X  also independent of  (X ?

Give proper justification and proof of your answer

___________________________________________________________________________

ANSWER

a)  If  R2  = R1  + R0 , meaning that  R1   is contained in R2  , then we can write

T = X R1  + (X R2  = XR1  + (X  (R1  + R0 ) = R1  (X + (X)   + (X R0  = R1   + (X R0  ,which is independent of   X

b) If  R1  = R2  + R0 , meaning that  R2   is contained in R1  , then we can write

T = X R1  + (X R2  = X(R2  + R0 ) + (X  R2   = R2  (X + (X)   + X R0  = R2   + X R0  ,which is independent of   (X.

c) If  R1  = R2  , then   T = R1  (X +(X)  = R1  ,which is independent of  X and (X.

_________________________________________________________________________

6.-  Design a gate combinational circuit, using AND, OR, NOT gates, that detects an error in the representation of a decimal digit coded in BCD code (Binary-Coded-Decimal). The output, E, of the circuit must be equal to  1  when the inputs contain any one of the six unused bit combinations in the BCD code. Otherwise, E assumes the value  0.

a) Give the truth table and k-map of  E

b) Give the minimal sum-of-products implementation of  E

c) The implementation you just found in part b) is not the absolute minimal two-level gate implementation of  E. Find an implementation of  E  using the fewest possible number of gates. (Only one OR gate and one AND gate are required for such implementation. Explain how you found it.

___________________________________________________________________________

ANSWER

---------------------------------------END OF ASSIGNMENT  #1-----------------------------------

# Text boxes

Complement

Dual

A(D

BCD

(A  B(C

(A +(C + D)

B

((A + C +(D)

(B(C D

(A B(D

A (B

B C D